True USB willem Universal Programmer Series Comparison Table

True USB GQ-4X - True USB GQ-3X - True USB GQ-2X

| Model | True USB GQ-4X | True USB GQ-3X | True USB GQ-2X |
| --- | --- | --- | --- |
| Programmer type | True USB | True USB | True USB |
| Other names/Alias | USB willem/ True USB PRO | USB willem/ True USB | USB Willem/ True USB |
| PC Interface/data communication | True USB:USB-USB | True USB:USB-USB | True USB:USB-USB |
| With own Enclosure | Yes | None | None |
| Support more DIP chips | Yes | - | - |
| Pin count ZIF socket | 40pin | 32pin | 32pin |
| Fully Automatic | Yes | Yes | No (Manual set needed) |
| Jumpers on board | None | None | None |
| Special developed software for True USB willem | Yes | Yes | Yes |
| CPLD JTAG Programming | Yes | No | No |
| Fast mode SPI devices (eg. SST25VF040B/80B/160B) | Yes | No | No |
| Free life-time software updates regularly | Yes | Yes | Yes |
| Total cable number required | One USB cable | One USB cable | One USB cable |
| Support 25VF series | Yes | Yes (partial) | No |
| Support 25LF series | Yes | Yes (partial) | No |
| Support TSOP48 | Yes | Yes | Yes |
| Support PSOP44 | Yes | Yes | Yes |
| Support 16bit | Yes | Yes | Yes |
| Dual Power supply capability | Yes (USB & AC/DC) auto detection/switching | Yes (USB & AC/DC) auto detection/switching | Yes (USB & AC/DC) |
| Supported Vcc range | 3.6V, 5V, 5.5V, 6.5V | 3.6V, 5V, 5.5V, 6.5V | 3.6V, 5V, 5.5V, 6.5V |
| Supported Vpp range | 0V,5V,12V,12.7V,15V,21V,25V | 0V,5V,12V,12.7V,15V,21V,25V | 0V,5V,12.7V,15V,21V,25V |
| Auto voltage Control | Yes | Yes | Yes |
| Working with laptop w/o parrellel port | Yes | Yes | Yes |
| Programmer Speed performance |  |  |  |
| Programming Speed sample (read) | 25 sec. for (AM29LV320) 13 sec. for (AT49LV1614) | 25 sec. for (AM29LV320) 13 sec. for (AT49LV1614) | - |
| Multi-tasking CPU usage | 10% | 10% | 10% |
| Support software O/S | Win98SE/Me/XP/NT/2k WindowVista | Win98SE/Me/XP/NT/2k WindowVista | Win98SE/Me/XP/NT/2k WindowVista |
| Allow User add device on software simply | Yes | Yes | Yes |
| Device search/ History memory | Yes | Yes | No |
| Works Stable with EPROMs | Yes | Yes | Yes |
| Mechanic DIP Switch/Electronics Switch on boardMCUmall© | None | None | Mechanic DIP Switch |
| Programmer board dimension~ (cm) | 15 x 9 x 2 | 15 x 8 x 1.5 | 15 x 8 x 1.5 |
| Working set weight(~) | ~250g | ~200g | ~190g |
| Status | Active | Active | Legacy |
| Manufacturer | MCUmall Electronics Inc. | MCUmall Electronics Inc. | MCUmall Electronics Inc. |