Willem Programmer Comparison Table:

True USB GQ-4X <->True USB GQ-3X <-> PCB5.5C <-> PCB5.0 C

| Model | True USB GQ-4X | True USB GQ-3X | Willem Parrellel PCB5.5C | Willem Parrellel PCB5.0C |
| --- | --- | --- | --- | --- |
| Programmer type | True USB | True USB | Parrellel | Parrellel |
| Other names/Alias | USB willem/ True USB PRO | USB willem/ True USB | Willem EPROM Pro Wilem Ultimate Window Willem PCB5.5C | Enhanced Dual Power Willem Willem PCB6.0 |
| PC Interface/data communication | True USB:USB-USB | True USB:USB-USB | Parrellel Printer Port | Parrellel Printer Port |
| With own Enclosure | Yes | None | None | None |
| Support more DIP chips | Yes | No | No | No |
| Pin count ZIF socket | 40pin | 32pin | 32pin | 32pin |
| Fully Automatic | Yes | Yes | No (Manual setup needed) | No (Manual setup needed) |
| Jumpers on board | None | None | Yes | Yes |
| Total jumber No. | Nil | Nil | Yes | Yes |
| Free life-time software updates regularly | Yes | Yes | No | No |
| Total cable number required | One USB cable | One USB cable | Two cables (USB & data cables) | Two cables (USB & data cables) |
| Dual Power supply capability | Yes (USB & AC/DC) auto detection/switching | Yes (USB & AC/DC) auto detection/switching | No (Single USB power) | Yes (USB & AC/DC) |
| Supported Vcc range | 3.6V, 5V, 5.5V, 6.5V | 3.6V, 5V, 5.5V, 6.5V | 5V,6.5V | 3.6V,5V,5.6V,6.2V |
| Supported Vpp range | 0V,5V,12V,12.7V,15V,21V,25V | 0V,5V,12V,12.7V,15V,21V,25V | 12V,15V,21V,25V | 12.7V,15V,21V,25V |
| Auto voltage Control | Yes | Yes | No | No |
| Working with laptop w/o parrellel port | Yes | Yes | No | No |
| Programmer Speed performance | Fastest | Fastest | Slow | Slow |
| Programming Speed sample (read) | 25 sec. for (AM29LV320) 13 sec. for (AT49LV1614) | 25 sec. for (AM29LV320) 13 sec. for (AT49LV1614) | 570 sec. for (AM29LV320) 285 sec. for (AT49LV1614) | 570 sec. for (AM29LV320) 285 sec. for (AT49LV1614) |
| Multi-tasking CPU usage | 10% | 10% | >98% | >98% |
| Support software O/S | Win98SE/Me/XP/NT/2k WindowVista | Win98SE/Me/XP/NT/2k WindowVista | Win98SE/Me/XP/NT/2k | Win98SE/Me/XP/NT/2k |
| Allow User add device on software simply | Yes | Yes | No | No |
| Device search/ History memory | Yes | Yes | No | No |
| Works Stable with EPROMs | Yes | Yes | No | Yes |
| Mechanic DIP Switch/Electronics Switch on boardMCUmall© | None | None | Electronics Switch | Mechanic DIP Switch |
| Programmer board dimension~ (cm) | 15 x 9 x 2 | 15 x 8 x 1.5 | 15 x 9 x 1.5 | 15 x 8 x 1.5 |
| Working set weight(~) | ~250g | ~200g | ~320g | ~190g |
| Status | Active | Active | Active | Legacy |
| Manufacturer | MCUmall Electronics Inc. | MCUmall Electronics Inc. | MCUmall Inc. affiliate | MCUmall Inc. affiliate |